## Slide 1: ESP32
Dr. Manel Puig i Vidal

## Slide 2
ESP32
The ESP32 is a popular and versatile microcontroller development board that is widely used for various Internet of Things (IoT) applications.
Some key features of the ESP32 board include:
Dual-Core Processor:
  Xtensa LX6 Microprocessor
  High processing power (up to 240 MHz clock speed)
Integrated Wi-Fi (802.11 b/g/n):
  2.4 GHz frequency band.
  Supports various Wi-Fi modes
    Station,
    Access Point,
    Station+AP.
  Enables seamless internet connectivity.
  3. Integrated Bluetooth (v4.2 BR/EDR and BLE):
    Bluetooth Classic and Bluetooth Low Energy support.
    Suitable for short-range communication and IoT applications.

## Slide 3
Integrated Peripherals:
  ADC (Analog-to-Digital Converter), DAC (Digital-to-Analog Converter).
  I2C (Inter-Integrated Circuit), SPI (Serial Peripheral Interface), UART (Universal Asynchronous Receiver-Transmitter) communication interfaces.
  PWM (Pulse Width Modulation), Timers, Capacitive Touch Sensors.
  GPIO (General Purpose Input/Output) pins for versatile interfacing.
Memory:
  SRAM (working memory): 520KB
  Flash memory (for storing the program code and data): 4MB, 8MB or 16MB
ESP32

## Slide 4
Low Power Consumption:
  making it suitable for battery-powered applications.
Rich Development Ecosystem:
  Well-supported by Espressif's ESP-IDF (IoT Development Framework).
  Arduino IDE compatibility for easier programming.
  Large community and extensive documentation.
Cost-Effective:
  Relatively low cost makes it accessible for hobbyists and professionals.
ESP32
https://docs.espressif.com/projects/arduino-esp32/en/latest/installing.html

## Slide 5
  Wi-Fi modes
    Station Mode (STA): In this mode, the ESP32 connects to an existing Wi-Fi network as a client.
    Access Point Mode (AP): In this mode, the ESP32 acts as a Wi-Fi hotspot, allowing other devices to connect to it. Station + Access Point Mode (STA+AP): This mode combines both Station and Access Point modes. The ESP32 can connect to an existing Wi-Fi network while simultaneously acting as a Wi-Fi hotspot for other devices.
ESP32
MQTT (Message Queuing Telemetry Transport):
Is a lightweight messaging protocol designed for machine-to-machine (M2M) communication and the Internet of Things (IoT).
Exemple: weather station that measures temperature and humidity:
  The weather station (a "client") "publishes" its readings to a topic called "weather/station1".
  Your phone and a display in your house (also "clients") "subscribe" to the "weather/station1" topic.
  The MQTT "broker" manage the topics and messaging transmission.
Everyone who's interested in the weather data gets it in real-time.
MQTT is a powerful tool for IoT solutions.

## Slide 6
Exemples:
Read IMU and send data to web server
Read IMU and publish data to topic using mqtt messaging protocol
  Create a webpage to subscribe to imu topic and publish data to webpage
  My labtop subscribes to the topic and print values using mqtt studio
Read IMU data and send data to:
  another ESP32 using ESP-now
  The 2nd esp32 send data in serial to PC
  Python program reads data and plot it on screen

## Slide 8
WiFi_SocketUDP_IMU

## Slide 9
ESP32_Receiver
ESP32_Sender
WiFi_SocketUDP_2_ESP32